Motorized Paper Shredder Machine

A paper shredder machine can be used to cut papers into small strips or pieces. These machines can be used by government associations or other privately-owned companies to destroy their private papers or confidential documents to avoid them from falling into wrong hands.

The Mini Paper Shredder provides following advantages including:

- Fully Motorized Operation

- Steel Blades for long life

- Geared design for high power cutting

- Easy to use compact machine

The paper shredder makes use of 2 x rutting blades to achieve the desired paper cutting. The blades are driven by a dc motor. The dc motor is attached to the blades through a bearing arrangement for high stability.

The motor is used to drive one blade which in turn drives the other blade using an equal gear mechanism. This ensures both blades move in desired direction and at the same speed. The shredder consists of a metal drawer with handle that allows user to pull out the shredded paper falling through the blades to be easily removed and disposed off.

The controller panel of the machine consists of switch for turning on and off the machine along with an emergency stop button to pause operation urgently. This we see a compact and portable motor driven paper shredder machine using geared mechanism for offices.

Components:

- Electric Motor

- Blades

- Gears

- Shaft

- Bearings

- Controller Circuitry

- Couplings

- Switches

- Handle

- Electrical & Wirings

- Mounts and Joints

- Supporting Frame

- Screws and Fittings

Applications:

- Paper Shredding

- Other Shredding

Advantages:

- Fully Motorized Operation

- Steel Blades for long life

- Geared design for high power cutting

- Easy to use compact machine

Disadvantages:

- Needs Power supply does not run on battery

- Cannot shred wood, plastic or metal scrap

Block Diagram:

Front View

Side View

3D View