Automatic Seed Sowing Robot

Sowing is the most important process in farming. It is a very tiring and time consuming process that requires a lot of human effort. Here we propose the design and fabrication of a fully automatic seed sowing robot that automates this task. The proposed robot uses four motors for running it in desired directions. We use a small bracket for pouring seeds. The robot consists of a funnel like arrangement in order to pour seeds into a lower container. There we use a shaft with gear like bucket teeth to pick up limited quantity of seeds and pour them on the ground in a steady manner in proper quantity. The front of the robot consists of a bent plate that drags on the soil to make a slot ahead of the machine before seeds are poured in it. The back portion of the robot consists of a tail like bent rod that is again used to pour soil on seeds sowed thus covering them with soil. Thus the system completely automated the seed sowing process using a smartly designed mechanical robotic system.

Components

- 12V motor

- Shaft

- Container

- Funnel

- Wheels

- Mounts

- Supporting Frame

- Joints & Fixtures

- Screws

Advantages

- Fully Automatic Seed Sowing

- Efficient and Fast Farming

- Portable Robot