# Object Counting Using 7 Segment Display

The project is designed to monitor the counting operations in industries. For example, products moving on a conveyor belt are counted by IR interruption concept and displayed on a seven segment display.
There are two pair sensors, each kept at certain distance from the other.

One pair of sensor consists of a transmitter and a receiver, kept exactly opposite to each other. The transmitting part emits modulated IR light which is received at the receiver end and fed to a microcontroller of 8051 family. When an object passes through the sensors then microcontroller gets interrupt signal (from IR sensors) and increments the count to displays it on 7 segments displays. Count down is also achieved if the object moves in reverse direction. This project can also be used in any public transport/trains to count the number of passengers for monitoring purpose.

Further the project can be enhanced by interfacing it with a warning system so that if total number of occupants in the vehicle exceeds the passenger carrying capacity then an alarm is generated by the device.

Block Diagram:

Hardware Specifications

- 8051 series Microcontroller

- Diodes

- 7-Segment Display

- Transistor

- LED

- IR LED’s

- Voltage Regulator

- IR Sensor

- Push button

Software Specifications

- Keil µVision IDE

- MC Programming Language: Embedded C