# Multi-Power Supply Using 4 Different Sources for No Break Power Supply

The project is designed to automatically supply continuous power to a load through one of the four sources of supply that are: solar, mains, generator, and inverter when any one of them is unavailable.
Four switches are used for four respective sources. These are connected to a microcontroller of 8051 family that provides input signals to it. Whenever a switch is pressed it shows the absence of that particular source. A relay driver is used that receives microcontroller generated output and switches that particular relay to provide continuous power supply. A lamp is used as a load for demonstration purpose which draws power from main. When main fails to supply power, automatically next available source is used say inverter. If inverter fails then the next one is used and so on. An LCD is also used to display which source is being currently used for power supply.
Therefore, this project provides an effective solution to provide an alternative power supply during frequent power cuts. In this project uses four switches to demonstrate the respective failure of that power supply. When any of the switches is pressed it shows the absence of that particular source, switches are connected to microcontroller as input signals. A microcontroller of 8051 family is used. The output of microcontroller is given to the relay driver IC, which switches appropriate relay to maintain uninterrupted supply to the load. The output shall be observed using a lamp drawing power supply from mains initially. On failure of the mains supply (which is actuated by pressing the appropriate switch) the load gets supply from the next available source, say an inverter. If the inverter also fails it switches over to the next available source and so on. The current status, as to which source supplies the load is also displayed on an LCD. As it is not feasible to provide all 4 different sources of supply, one source with alternate switches are provided to get the same function.

Block Diagram:

Hardware Specifications

- 8051 series Microcontroller

- Relay Driver IC

- Relays

- Crystal

- LCD

- Transformer

- Diodes

- Lamp

- Push Buttons

- LEDS

- Voltage Regulator

Software Specifications

- Keil µVision IDE

- MC Programming Language: Embedded C