# Remote Vehicle Control Through Cell Phone Using DTMF

The proposed project aims to drive a vehicle using a mobile phone. The project requires two mobile phones, one to control the robot that sends DTMF commands to another one mounted on the robot vehicle. A DTMF decoder interfaced with the microcontroller of 8051 family receives the commands and with the help of a motor driver operates the vehicle movement. Thus according to the commands sent from the phone two DC motors enables the vehicle movement through motor driver IC. A battery is used for power source.

Block Diagram:

Hardware Specifications

- 8051 series Microcontroller

- DTMF Decoder IC

- Motor Driver IC

- DC Motors

- Batteries

- Robot Body

- Crystal

Software Specifications

- Keil µVision IDE

- MC Programming Language: Embedded C