Android Controlled Fire Fighter Robot

Our proposed project aims to develop an android controlled fire fighter robot that can be used to extinguish fires through remote handling. The vehicle consists of a water tank along with a pump which can throw water when needed. The system uses an 8051 microcontroller for this purpose. The android device is used as a transmitter to send over controlling commands to the vehicle. The android device provides a good touch based gui for controlling the robotic vehicle.
The Bluetooth receiver on the vehicle is used to receive those commands sent by the android device. These are then fed to the motors responsible for controlling the vehicle movements in front, back, left and right directions.
The Bluetooth receiver is interfaced with an 8051 microcontroller for this purpose. The microcontroller after receiving input commands, operates the motors through a driver IC for vehicle movements.
The use of android has one more advantage in addition to improved GUI. It allows use of Bluetooth technology for communication allowing the vehicle to operate in a good range from the device. The system can also be later enhanced through the use of a wireless camera to be used for monitoring purposes.

BLOCK DIAGRAM:

Hardware Specifications 8051 Family Microcontroller Bluetooth Decoder Motor Driver IC DC Motors Batteries Robotic Body Water Tank Bluetooth Device.

Software Specifications Keil µVision IDE MC Programming Language: Embedded C

Bluetooth Overview

Hardware features

Typical -80dBm sensitivity

Up to +4dBm RF transmit power

Low Power 1.8V Operation ,1.8 to 3.6V I/O

PIO control

UART interface with programmable baud rate

With integrated antenna

With edge connector

- Wireless technology for short-range voice and data communication

- Low-cost and low-power

- Provides a communication platform between a wide range of “smart” devices

- Not limited to “line of sight” communication

It is preferable to use bluetooth because nowadays people have their smartphones with them all the time, since the smartphones have bluetooth facility in them, thus it's better to use bluetooth rather than using RF remotes or IR remotes. Have you ever seen people carrying remotes???

Using bluetooth has many of its own advantages :
1.It's secure.
2.Easy to use.
3.It works in short distance range(i.e. upto 10mtrs.)
4.Anyone can find free bluetooth apps on android and many more.