Mobile Charging On Coin Insertion

The aim of this project is to provide a solution for charging of mobile at public places. The person who wants to charge his/her mobile has to insert a coin and connect his/her mobile with the charger. Mobile will be charged a particular amount of time depending on the number of coins inserted by him/her. As soon Coin Sensor detects the coin it sends a pulse to the Microcontroller. The Microcontroller turns ON the relay(Electromechanical Switch) to provide 230V,50Hz signal to the charging socket and the user can charge his/her mobile phone from the socket. The LCD (16×2) is used to display the time duration for which the user can charge his/her mobile phone. As the total time gets lapsed, the charging will be stopped. It can be further explained with the help of following block diagram.

Block Diagram

- Hardware Specifications

- Atmega Microcontroller

- LCD’s

- Coin Sensor

- Crystal Oscillator

- Resistors

- Capacitors

- Transistors

- Cables and Connectors

- Diodes

- PCB and Breadboards

- LED

- Transformer/Adapter

- Push Buttons

- Switch

- IC

- IC Sockets

- Software Specifications

- Arduino Compiler

- MC Programming Language: C

ATmega328

The Atmel 8-bit AVR RISC-based microcontroller combines 32 KB ISP flash memory with read-while-write capabilities, 1 KB EEPROM, 2 KB SRAM, 23 general purpose I/O lines, 32 general purpose working registers, three flexible timer/counters with compare modes, internal and external interrupts, serial programmable USART, a byte-oriented 2-wire serial interface, SPI serial port, 6-channel 10-bit A/D converter (8-channels in TQFP and QFN/MLF packages), programmable watchdog timer with internal oscillator, and five software selectable power saving modes. The device operates between 1.8-5.5 volts. The device achieves throughputs approaching 1 MIPS per MHz.

### Features

- High Performance, Low Power AVR® 8-Bit Microcontroller

– Advanced RISC Architecture

– 131 Powerful Instructions

– Most Single Clock Cycle Execution

– 32 x 8 General Purpose Working Registers

– Fully Static Operation

– Up to 20 MIPS Throughput at 20 MHz

– On-chip 2-cycle Multiplier

- Flash Program Memory: 32 kbytes

- EEPROM Data Memory: 1 kbytes

- SRAM Data Memory: 2 kbytes

- I/O Pins: 23

- Timers: Two 8-bit / One 16-bit

- A/D Converter: 10-bit Six Channel

- PWM: Six Channels

- RTC: Yes with Separate Oscillator

- MSSP: SPI and I²C Master and Slave Support

- USART: Yes

- External Oscillator: up to 20MHz

LCD

LCD's typically have 14 data pins and 2 for the LED backlight. Character LCDs use a standard 14-pin interface and those with backlights have 16 pins. There may also be a single backlight pin, with the other connection via Ground or VCC pin. The two backlight pins may precede the pin 1.The nominal backlight voltage is around 4.2V at 25˚C using a VDD 5V capable model. Character LCDs can operate in 4-bit or 8-bit mode. In 4 bit mode, pins 7 through 10 are unused and the entire byte is sent to the screen using pins 11 through 14 by sending 4-bits) at a time.

COIN SENSOR

A coin acceptor validates a coin/token based on physical properties such as weight, size and/or magnetic content and then sends a corresponding I/O signal to its output connector.

COIN ACCEPTOR TECHNOLOGIES:

Reference

http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=7375261&queryText=mobile%20charging%20coin&newsearch=true