# Long Range Spy Robot with Metal Detection

This system Long Range Spy Robot with Metal Detection is a very innovative system as this system allows operating a robot irrespective of the distance of the user who wants to operate the robot. The user of this system doesn’t have to worry about the distance in order to operate the robot. The system does this with the help of DTMF technology which allows sending data commands via a call. The user wishing to operate the robot will just have to call on the mobile phone connected to this system. This system consists of 8051 family microcontroller which is interfaced to the metal detector, spy camera and the system also uses battery. The metal detector helps to detect metal on turns on the buzzer.

In order to operate the system, the user has to make a call to the phone connected to this robot and once the call is received, the user will have to use the keypad to send data commands to the robot. The data commands will make the robot to either go in forward, backward, left or right direction. The system makes use of night vision enabled spy camera with the help of which the user can view the area captured by this spy camera which will be mounted on this robot. The user will be able to view the area captured by this spy camera not only during day time but also during night. All the area captured by this spy camera can be viewed in PC.

Thus with the help of this DTMF technology, the user of this system can operate the robot via data commands send through mobile phone, irrespective of the distance from the robot.

# Block Diagram:

Hardware Specifications

- 8051 Microcontroller

- Wireless Camera

- Metal Detector

- Buzzer

- Robot Body

- Motor Driver IC

- DC Motors

- Diodes

- Voltage Regulator

- Resistors

- Capacitors

- LED

Software Specifications

- Keil µVision IDE

- MC Programming Language: Embedded C

Dual-tone multi-frequency signaling (DTMF) is an in-band telecommunication signaling system using the voice-frequency band over telephone lines between telephone equipment and other communications devices and switching centers. DTMF was first developed in theBell System in the United States, and became known under the trademark Touch-Tone for use in push-button telephones supplied to telephone customers, starting in 1963. DTMF is standardized by ITU-T Recommendation Q.23. It is also known in the UK as MF4.

The Touch-Tone system using a telephone keypad gradually replaced the use of rotary dial and has become the industry standard forlandline and mobile service. Other multi-frequency systems are used for internal signaling within the telephone network.

DTMF (Dual tone multi frequency) as the name suggests uses a combination of two sine wave tones to represent a key. These tones are called row and column frequencies as they correspond to the layout of a telephone keypad.

A DTMF keypad (generator or encoder) generates a sinusoidal tone which is mixture of the row and column frequencies. The row frequencies are low group frequencies. The column frequencies belong to high group frequencies. This prevents misinterpretation of the harmonics. Also the frequencies for DTMF are so chosen that none have a harmonic relationship with the others and that mixing the frequencies would not produce sum or product frequencies that could mimic another valid tone. The high-group frequencies (the column tones) are slightly louder than the low-group to compensate for the high-frequency roll off of voice audio systems.

The row and column frequencies corresponding to a DTMF keypad have been indicated in the above figure.

Reference

- http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=7475162&newsearch=true&queryText=spy%20robot%20metal