# Contactless Switch for Homes and Offices

Contact switches are today the most common method used for switching off home appliances, lights, fans. Etc. But are they the most efficient way for load switching ? Well here are some disadvantages for traditional switches:

- Toggle switches are based on physical press hence have a limited lifetime

- One switch can operate only one load hence we need large switchboards

- These switches are not contactless so prone to wear and tear

How about we design a switching system that overcomes all these issues with a more modern yet low cost system. We hereby design a single switch that can operate 4 loads and that too without the user ever needing to touch the switch.

The system is made using a STM32 controller that is used to operate an gesture based switch. It is also integrated with a sound sensor for even faster operation speed and ease of use.

The system is used to operate 4 loads at a time using single switch. The controller constantly monitors the gesture sensor for any human gestures. Hand gestures made within 5 – 10 centimeters proximity of the sensor are sensed by the system.

As soon as a gesture is sensed the controller operates the relay board to switch On or OFF the respective load as per gesture. Also the user may just clap anywhere near the switch n order to switch ON or OFF all loads at a clap.

The system operates loads using relay board in following manner

- Left Swipe >> Light 1 Switching

- Right Swipe >> Light 2 Switching

- Up Swipe >> Fan 1 Switching

- Down Swipe >> Fan 2 Switching

- Clap >> All Loads Switching Together

This allows for an ultra-modern yet space saving, futuristic switching system that may one day replace all traditional switches.

Components

- STM 32 Controller

- Gesture Sensor

- Sound Sensor

- Relay Module

- 2 x Light Bubs

- 2 x Mini Fans

- Push Buttons

- LED’s

- PCB Board

- Resistors

- Capacitors

- Transistors

- Cables and Connectors

Block Diagram