# Automatic Stamping Labeling Machine Using PLC

Overview:

All product automation processes require stamping as a last step to brand the finished product. Different types of products require different types of stamps. Here we demonstrate a complete stamping system that stamps the logo on the finished product.

The system is automated and controlled by PLC. The system consists of a conveyor belt driven by a DC motor. The process is started using a start push button, and when the product reaches the stamping base, the sensor senses the product and the stamp mounted on the pneumatic cylinder is activated with the help of a solenoid valve which initiates the stamping process. After this the final stamped product is moved ahead and collected in the tray.

Block Diagram:

Components/Instrumentation:

- Allen Bradley Programmable Logic Control(PLC)

- Push Buttons

- Led’s

- Relay card

- Metal Detector Sensor

- IR Sensor

- Self inked stamp

- Conveyor Belt

- DC Motor – Buy DC Motors Online

- Pneumatic Cylinders – Buy Pneumatic Cylinders Online

- Pneumatic Pipes – Buy Pneumatic Pipes Online

- Pneumatic Fittings – Buy Pneumatic Fittings Online

- Solenoid Valves – Buy Pneumatic Valves Online

- Brackets & Mounts

- Supporting Frame

- Joints & Fixtures

- Couplings – Buy Couplings Online

- Screws & Bolts

Software Specifications:

- Connected Components Workbench

- Ladder Logic