Automated Drain/Gutter Cleaner Project

Cleaning of drains/gutters has always been a problem. Labors cleaning gutters & drain seems unethical and also leads to a high risk of them catching infections or poisoning due to large amounts of waste/chemicals in them. Also throwing of bottles/plastics and other such objects into the gutters lead to narrowing and eventually blockage in gutter flow. This leads to overflow in many cases. So here we provide a fully automated drain gutter cleaning mechanism to tackle these modern day gutter jamming issues. Our system uses an automated gutter/drain cleaning system that lets fluids flow through it but catches large solid waste like bottles & plastic and accumulates it. So gutter cleaners need to just clean these gutter cleaning systems installed at points instead of cleaning entire gutter floors. Our system consists of metal teeth based jaws that wait at the bottom of the mechanism. It is mounted in a frame to hold the system upright in the gutter. The vertical frame bed is used to let liquid flow but catch all solid waste. The mechanism consists of a filter basket on top of it. After particular time intervals the jaw lifts up using a motorized shaft which is connected using a chain to the jaws. It then reaches the top and turns upside down to dump the solid waste. Now after dumping the waste, the motor rotates again to bring the jaw again to the bottom position to collect more waste. The system is a very efficient way to cleaning gutters & drains and also requires very low power since it will only rotate once or twice a day to dump the solid waste.

Components

- Collector Jaw

- Frame Bed

- Mounts

- Chain

- Shafts

- Collector Bin

Advantages

- Automated Cleaning

- Automatic Waste Collection

- Low Power Consumption

Side Views